## Slide 1: Packet Radio Communications

## Slide 2: Objective
Understand how a Packet communications station works,
Understand how to set-up a Packet communications station,
Understand how to operate it
BUILD ONE!!!!!

## Slide 3: Two Session Talk
First Session – Digital Transmission & Reception Concepts
Second Session - Hands-on Set-up your own radio

## Slide 4: Talk Outline
Concepts Session
  Overview of Packet Radio Communications
  Terms:
    Digital
    Packet
    BIT
    BYTE
    BAUD
    TNC
    MODEM
  Overview of Packet Radio Relaying
  How digital communications are sent over Amateur Radio Frequencies
  Radio Messaging System
  Preview of required equipment and software required to perform digital communications in the VHF (2 Meter) & UHF (70 cm) Ham Radio Bands
Demonstrate Software installation & configuration
Hands-on Workshop
  Install Software
  Connect computer to radio through supporting equipment
  Send Mail

## Slide 5: Packet Radio Communications
What is it?
  For us, it’s a method of sending and receiving email messages, chat texts, even photos & documents over your radio to another radio or for retrieval via the internet.

## Slide 6: Let’s back up a bit ….
What is “DIGITAL”
  In the context of both computers & digital communications, digital means data expressed as series of 0’s and 1’s called ….
        BINARY numbers
What are and Why use Binary numbers?
  Binary numbers easily represent something that is either ON or OFF
    Examples
      A Light bulb
      An ON/OFF switch
      A single transistor in an electronic circuit
  They can also easily represent something that has two states or conditions
      Morse Code -> DOT or DASH
      Audio tone -> A LOW / HIGH pitch audio Tone
This is where we are headed

## Slide 7: Light Bulb Example
Let’s assign 1 and 0 to the light bulb state
  Light bulb ON = 1
  Light bulb OFF = 0
Tah Dah!!!! Voila!! A binary system in your living room

## Slide 8: A bit more binary
  Now let’s say we have 3 light bulbs
    And agree that
      Bulb 1 has a weight of 1 when ON, but 0 when OFF
      Bulb 2 has a weight of 2 when ON, but 0 when OFF
      Bulb 3 has a weight of 4 when ON, but 0 when OFF
Bulb 3 | Bulb 2 | Bulb 1 | Binary Number | Decimal Number
OFF | OFF | OFF | 0 0 0 | 0
OFF | OFF | ON | 0 0 1 | 1
OFF | ON | OFF | 0 1 0 | 2
OFF | OFF | OFF | 0 1 1 | 3
ON | OFF | OFF | 1 0 0 | 4
ON | OFF | ON | 1 0 1 | 5
ON | ON | OFF | 1 1 0 | 6
ON | ON | ON | 1 1 1 | 7

## Slide 9: Binary Representation
  Example of 1’s & 0’s representation
  By convention (fancy word for agreement)
    The letter ‘A’ is represented by decimal number 65 and binary number 01000001
    The letter ‘B’ is represented by decimal number 66 and binary number 01000010
    The letter ‘C’ is represented by decimal number 67 and binary number 01000011
    The letter ‘D’ is represented by decimal number 68 and binary number 01000100
    The letter ‘E’ is represented by decimal number 69 and binary number 01000101
  There is a representation for every character on your keyboard

## Slide 10: ASCII TABLE
Character | Digital Representation | Character | Digital Representation | Character | Digital Representation
Space | 0100000 | @ | 01000000 | ` | 01100000
! | 0100001 | A | 01000001 | a | 01100001
" | 0100010 | B | 01000010 | b | 01100010
# | 0100011 | C | 01000011 | c | 01100011
$ | 0100100 | D | 01000100 | d | 01100100
% | 0100101 | E | 01000101 | e | 01100101
& | 0100110 | F | 01000110 | f | 01100110
' | 0100111 | G | 01000111 | g | 01100111
( | 0101000 | H | 01001000 | h | 01101000
) | 0101001 | I | 01001001 | i | 01101001
* | 0101010 | J | 01001010 | j | 01101010
+ | 0101011 | K | 01001011 | k | 01101011
, | 0101100 | L | 01001100 | l | 01101100
- | 0101101 | M | 01001101 | m | 01101101
. | 0101110 | N | 01001110 | n | 01101110
/ | 0101111 | O | 01001111 | o | 01101111
0 | 0110000 | P | 01010000 | p | 01110000
1 | 0110001 | Q | 01010001 | q | 01110001
2 | 0110010 | R | 01010010 | r | 01110010
3 | 0110011 | S | 01010011 | s | 01110011
4 | 0110100 | T | 01010100 | t | 01110100
5 | 0110101 | U | 01010101 | u | 01110101
6 | 0110110 | V | 01010110 | v | 01110110
7 | 0110111 | W | 01010111 | w | 01110111
8 | 0111000 | X | 01011000 | x | 01111000
9 | 0111001 | Y | 01011001 | y | 01111001
: | 0111010 | Z | 01011010 | z | 01111010
; | 0111011 | [ | 01011011 | { | 01111011
< | 0111100 | ] | 01011100 | ¦ | 01111100
= | 0111101 | \ | 01011101 | } | 01111101
> | 0111110 | ^ | 01011110 | ~ | 01111110
? | 0111111 | _ | 01011111 | delete | 01111111
American Standard Code
for
Information Interchange
ASCII for short

## Slide 11: Digital Communications
Transmitting 1’s & 0’s over ham radio frequencies
  Convert 1’s & 0’s to audio
    Assign a unique tone to 0 & 1
      0 = 2200 Hz tone
      1 = 1200 Hz tone

## Slide 12: Play Live Audio Tones

## Slide 13: Tone Encode the character ‘E’

## Slide 14: Tone Encode & Decode
Sound
Card
Sound
Card

## Slide 15: Let’s digress for a moment
To talk about BITS & BYTES

## Slide 16: Bits and Bytes
0 1 0 0 0 0 1 0 1
A Single Digit is a ‘bit’
8 bits make a ‘byte’

## Slide 17: Bit Rate and BAUD
Transmission Speed is expressed in bit/second
6.66666 milliseconds

## Slide 18: Let’s take a break

## Slide 19: Back to Tone Encode & Decode

## Slide 20: Terminal Node Controller
TNC for short

## Slide 21: Terminal Node Controller
A TNC takes raw digital data such as characters in an e-mail message
  divides the characters in an e-mail message into small segments,
  converts the character to binary 8 bit bytes
  adds some extra bits of information (no pun intended) to provide an error checking / detecting / correcting scheme, and puts those into “packets” data
  then converts those packets, bit by bit, into audio tones

## Slide 22: Details on Data packing

## Slide 23: Details on Data packing
This is a topic for a later day for anybody that is interested

## Slide 24: Where is the Terminal Node Controller located?
There are multiple configurations of a combination of hardware & software that make up TNC functionality
  Sometimes it’s built into the radio ( such as the Yaesu FT-991A)
  Sometimes it’s totally contained within an electronics box inserted between a personal computer and a radio
  Sometimes various functions of the TNC is split between software on a personal computer and a sound card.

## Slide 25: Terminal Node Controller in the radio
010000101
010000101
E
E

## Slide 26: Terminal Node Controller in a Box
TNC
TNC
010000101
010000101
E
E

## Slide 27: A Terminal Node Controller TNC that is split between software on a personal computer and a sound card.
Sound
Card
Sound
Card
010000101
010000101
E
E

## Slide 28: Hardware Example with specific products for
the third configuration where the TNC functionality is split between software on a personal computer and a sound card.

## Slide 29: Example Client Hardware Set up
010000101

## Slide 30: Radio Networking Architectures

## Slide 31: Radio Mail Networking Architectures
Peer To Peer
Mail Server
Gateway
Telnet

## Slide 32: Peer to Peer Topology
Message Server
Sound
Card
Sound Card
Sound Card
010000101
010000101
E
E

## Slide 33: Peer To Peer Limitations
Advantages
  Simplest architecture
Limitations
  Can only send an email to one station at a time
  Both station operators are required to be operating their stations at the same time in order to send a message

## Slide 34: Radio Mail Server Architecture
Linda
Clint
Ken
TNC
TNC
TNC
TNC
Bruce
TNC
Local
Radio Mail Server
Mail is sent to the Local Radio Mail Server and stored until it is picked up by destination address
Ability to send one message to multiple stations

## Slide 35: Gateway Expanded Radio Mail Server Network

## Slide 36: Extended Radio Mail Service
Linda
Clint
Ken
TNC
TNC
TNC
TNC
Bruce
TNC
CMS
TNC
Message Gateway
TNC
TNC
Message Gateway

## Slide 37: Telnet Architecture
CMS

## Slide 38: Next Session Preview

## Slide 39: Next Session Preview
Hands-on Workshop
  Install Software
  Connect computer to radio through supporting equipment
  Learn how to use Software
  Send and Receive Mail
This is where we’re headed

## Slide 40: Recommended Equipment For Next Session
Radio without built in sound card nor TNC
  VHF and/or UHF mobile or base station
    Use of handheld transceivers is possible but not recommended to start with
Computer
  Windows 10 or later operating system
    With at least 3 USB ports
Sound card
  TigerTronics SignalinkTM USB
      https://tigertronics.shop/shop/ols/categories/signalink-usb
Cables
  USB Cable from computer to SignaLinkTM sound card
    Provided in the with the SignaLinkTM sound card
  Cable from the sound card to the radio
    This cable type & make is dependent on the radio
      TigerTronics has a list of cables for popular radios in the .pdf file called “SignaLink USB Product Guide”
      Note to Bruce: Print out Product Guide
      Web link is : https://tigertronics.com/files/SignaLink%20USB%20Product%20Guide.pdf
Radio with built in sound card / TNC
  VHF and/or UHF mobile or base station
    Use of handheld transceivers is possible but not recommended to start with
Computer
  Windows 10 or later operating system
    With at least 3 USB ports
Cables
  Need the correct cable that goes from the computer USB port to the RADIO’s TNC or data port

## Slide 41: Let’s take a look at the Signalink website
It’s made by a company called Tigertronics
  https://tigertronics.com/
And Download the product selector guide
  https://tigertronics.com/files/SignaLink%20USB%20Product%20Guide.pdf
And then let’s shop
  https://tigertronics.shop/

## Slide 42: Questions

## Slide 43: Session 2

## Slide 44: Installing Winlink to work with Radio for RMS (Radio Mail Service)

## Slide 45: Review: Where is the Terminal Node Controller located?
There are multiple configurations of a combination of hardware & software that make up TNC functionality
  Sometimes it’s built into the radio ( such as the Yaesu FT-991A)
  Sometimes it’s totally contained within an electronics box inserted between a personal computer and a radio
  Sometimes various functions of the TNC is split between software on a personal computer and a sound card.

## Slide 46: Let’s focus on…
the third configuration where the TNC functionality is split between software on a personal computer and a sound card.

## Slide 47: Example Client Hardware Set up
010000101
Distributed TNC Function

## Slide 48: Ordering Signalink USB sound card with correct cables

## Slide 49: Connect Signalink USB sound card

## Slide 50: Software
Soundmodem
  Converts digital data to binary frequencies for use on “Packet Radio”
RMS Express (aka Winlink, aka Winlink Express)
  User Interface software
    with e-mail creation, radio connection, message send & receive
VARA FM (optional)
  Converts digital data to binary frequencies for use on “VARA Packet Radio”

## Slide 51: Soundmodem Download & Install
Go to the (C:) folder aka “root folder” and create a new folder and change its name to SoundModem

## Slide 52: Soundmodem Download & Install
  Go to webpage  http://uz7.ho.ua/packetradio.htm

## Slide 53: Soundmodem Download & Install
Scroll down until you see the link labeled soundmodem114.zip or similar (“114” is the version number and may change) and click on it

## Slide 54: Soundmodem Download & Install
    Move the soundmodem114.zip file from the Downloads file to the C:\SoundModem folder.
    Extract the .zip file into the C:\SoundModem folder.

## Slide 55: Connect Computer, SignaLink Sound Card & Radio
Different for every computer

## Slide 56: Adjust Audio Playback & Recording Devices

## Slide 57: Adjust Audio Playback & Recording Devices
Open the Sound Control Panel

## Slide 58: RMS Express (aka Winlink, aka Winlink Express) Download & Install
  Go to website  https://www.winlink.org/ and click on “Download”

## Slide 59: RMS Express (aka Winlink, aka Winlink Express) Download & Install
Click on “User Program”

## Slide 60: RMS Express (aka Winlink, aka Winlink Express) Download & Install
Click on “Winlink_Express_install_1-7-21-0.zip”

## Slide 61: RMS Express (aka Winlink, aka Winlink Express) Download & Install
Go to Downloads folder and extract the contents of the .zip file

## Slide 62: RMS Express (aka Winlink, aka Winlink Express) Download & Install
Click on “Winlink_Express_install.exe”

## Slide 63: RMS Express (aka Winlink, aka Winlink Express) Download & Install
This is a false warning. Click “More_info”

## Slide 64: RMS Express (aka Winlink, aka Winlink Express) Download & Install
Click “Run anyway”

## Slide 65: VARA FM (optional)
    Go to webpage  https://downloads.winlink.org/VARA%20Products/
    Download the file VARA%20FM%20v4.3.8%20setup.zip
    Extract and run the installation VARA%20FM%20setup%20 (Run%20as%20Administrator).exe similar to method used to install RMS winlink

## Slide 66: Run and configure RMS Express (aka Winlink, aka Winlink Express)
After installation is complete, find either the
  Winlink Express icon
    or the
  RMS Express icon
on your computer Desktop screen and double click it

## Slide 67: Here’s mine

## Slide 68: Configure Winlink Express
  Under the Setting tab, select Winlink Express Setup….

## Slide 69: Configure Winlink Express
  Fill out the Winlink Express Properties page with you callsign, address and grid square location etc….
  When finished click update

## Slide 70: Configure Winlink Express
  Click on the drop down list to the right of “Open Session:” and select “Packet Winlink”

## Slide 71: Configure Winlink Express
  Click on “Open Session:”

## Slide 72: Configure Winlink Express
Click on Settings

## Slide 73: Packet Setup
Change settings to match what is shown here

## Slide 74: BACKUP SLIDES
Technical and whys

## Slide 75: Packet Radio Communications

## Slide 76: A word about Packet radio relay
Winlink
The CMS station

## Slide 77: Digression about what is a TNC

## Slide 78: What does a Terminal Node Controller Do?
A Terminal Node Controller
  converts text characters into a series of 1’s & 0’s
  Then converts the 1’s & 0’s into audio tones for transmission over the radio.
Example
  1’s & 0’s representation
    Letter A is represented by the series 01000001
    Letter B is represented by the series 01000010
    Letter C is represented by the series 01000011
  Convert 1’s & 0’s to audio
    0 = 2200 Hz tone
    1 = 1200 Hz tone

## Slide 79: My Dig Comm station with Distributed TNC
Uses…
  Hardware
    A TH 7800 2 meter radio made by TYT
    A Signalink USB sound card from Tigertronics
    A personal Computer with the following software:
  Software
    Winlink Express ( aka RMS express)
    A program called “soundmodem”
  All the above software is free

## Slide 80: Winlink -> Peer to Peer Session - > soundmodem
Winlink
soundmodem
Peer to Peer
Session

## Slide 81: Compose an Email