## Slide 1: Sangre de Cristos Amateur Radio Club Packet Radio Comms Session II
Installing Winlink to work with Radio for Radio Mail Service (RMS)

## Slide 2: Objectives

## Slide 3: Objectives
Download, install & configure Winlink Client Software and supporting modem software
Configure Hardware
  Radio
  Computer
  Terminal Network Controller
Compose an E-mail message & send through your radio to a local Winlink mail server / Gateway

## Slide 4: Recommended Equipment For this Session
Radio without built in sound card nor TNC
  VHF and/or UHF mobile or base station
    Use of handheld transceivers is possible but not recommended to start with
  Computer
    Windows 10 or later operating system
      With at least 3 USB ports
  Sound card
    TigerTronics SignalinkTM USB
  Cables
    USB Cable from computer to SignaLinkTM sound card
      Provided in the with the SignaLinkTM sound card
    Cable from the sound card to the radio
Radio with built in sound card / TNC
  VHF and/or UHF mobile or base station
    Use of handheld transceivers is possible but not recommended to start with
  Computer
    Windows 10 or later operating system
      With at least 3 USB ports
  Cables
    Need the correct cable that goes from the computer USB port to the RADIO’s TNC or data port

## Slide 5: Review: Where is the Terminal Node Controller located?
There are multiple configurations of a combination of hardware & software that make up TNC functionality
  Sometimes it’s built into the radio ( such as the Yaesu FT-991A)
  Sometimes it’s totally contained within an electronics box inserted between a personal computer and a radio
  Sometimes various functions of the TNC is split between software on a personal computer and a sound card.

## Slide 6: Review: Where is the Terminal Node Controller located?
There are multiple configurations of a combination of hardware & software that make up TNC functionality
  Sometimes it’s built into the radio ( such as the Yaesu FT-991A)
  Sometimes it’s totally contained within an electronics box inserted between a personal computer and a radio
  Sometimes various functions of the TNC is split between software on a personal computer and a sound card.
Let’s focus on this configuration

## Slide 7: Third Configuration - TNC split between software on PC and a soundcard
010000101
Distributed TNC Function

## Slide 8: Software Download & Install

## Slide 9: Software
Two Software application to install are:
  Soundmodem
    Converts digital data to binary frequencies for use on “Packet Radio”
  Winlink Express
    User Interface software
      with e-mail creation, radio connection, message send & receive

## Slide 10: Download & Install SoundModem

## Slide 11: Soundmodem - Download & Install
Go to the (C:) folder aka “root folder” and create a new folder and change its name to SoundModem

## Slide 12: Soundmodem Download & Install
  Go to webpage  http://uz7.ho.ua/packetradio.htm

## Slide 13: Soundmodem Download & Install
Scroll down until you see the link labeled soundmodem114.zip or similar (“114” is the version number and may change) and click on it in order to download

## Slide 14: Sound Modem Download & Install
Find the soundmodemxxx.zip file by navigating to your Downloads Folder

## Slide 15: A word about .zip folders
A folder with .zip suffix is a compressed file or collection of files and the contents must be decompressed and extracted in order to use.
This process is referred to as extracting or unzipping
To unzip (extract) on Windows 7 or later systems
  Locate the zipped folder that you want to unzip (extract) files or folders from.
  Do one of the following:
    To unzip a single file or folder, double click on the zipped folder in order to open it and see the contents, then drag the file or folder from the zipped folder to a new location.
    or
    To unzip all the contents of the zipped folder, press and hold (or right-click) the folder, select Extract All..., and then follow the instructions.

## Slide 16: How to Extract All
Select the .zip file then…
Click on “Extract All”

## Slide 17: Soundmodem Download & Install
    Move the soundmodem114.zip file from the Downloads file to the C:\SoundModem folder.
    Extract the .zip file into the C:\SoundModem folder.

## Slide 18: Download & Install Winlink Express

## Slide 19: RMS Express (aka Winlink, aka Winlink Express) Download & Install
  Go to website  https://www.winlink.org/ and click on “Download”

## Slide 20: RMS Express (aka Winlink, aka Winlink Express) Download & Install
Click on “User Program”

## Slide 21: RMS Express (aka Winlink, aka Winlink Express) Download & Install
Click on “Winlink_Express_install_1-7-21-0.zip”

## Slide 22: RMS Express (aka Winlink, aka Winlink Express) Download & Install
Go to Downloads folder and extract the contents of the .zip file

## Slide 23: RMS Express (aka Winlink, aka Winlink Express) Download & Install
Click on “Winlink_Express_install.exe”

## Slide 24: RMS Express (aka Winlink, aka Winlink Express) Download & Install
This is a false warning. Click “More_info”

## Slide 25: RMS Express (aka Winlink, aka Winlink Express) Download & Install
Click “Run anyway”

## Slide 26: Now let’s Connect Computer, SignaLink Sound Card & Radio
Different for every computer

## Slide 27: Before connecting SignaLink to your computer
Let’s Open the Device manager……….

## Slide 28: Opening Device Manager
First,
Press the Windows Key and type “Device Manager”
Second,
Click on “Device manager”

## Slide 29: Device Manager
Look for “Audio inputs and outputs” in Device Manager and double click on it to expand

## Slide 30: Device Manager
Note Audio Devices

## Slide 31: Connect SignaLink to Computer
Plug in the Signal Link USB cable in between the SignaLink and the computer and turn on

## Slide 32: New Audio Devices appear in Device Manager
Before Plugin
After Plugin
Notice the
New Audio Devices here on the right

## Slide 33: Restore Windows System default Audio Devices

## Slide 34: Windows Automatic USB Device Detection/Selection
When a new USB audio device is plugged into a Window Operating System based computer, (as we just did) the Windows Operating System assumes the user wants to use that audio device as the system default audio device.
This is an incorrect action on part of the operating system when a modem sound card such as SignaLink USB is attached.
  So, the default audio devices must be restored for normal computer operations and so that the radio will not transmit normal computer sounds

## Slide 35: Restore System default audio devices (continued)
Using the Windows Operating System Sound Control Panel

## Slide 36: Open Sound Control Go to lower right hand corner of desktop

## Slide 37: Sound Control
Right Click on Speaker Icon

## Slide 38: Sound Control
Select Sounds

## Slide 39: Restore System default audio Playback device
Highlight your normal audio output Devices & click on
“Set Default”

## Slide 40: Restore System default audio Recording device
Highlight normal microphone input device & click on
“Set Default”

## Slide 41: Adjust SignaLink Audio Levels
For radio operation

## Slide 42: Adjusting Receive Volume on SignaLink Soundcard
Reopen the Sound Control Panel go to Recording tab
Double Click what ever audio device the SignaLink soundcard is for your computer

## Slide 43: Note to Bruce: Add recording level adjust slide
Select “Levels” tab
Slid Line volume to 100

## Slide 44: Winlink Express Software
Launch & Configure

## Slide 45: Start Winlink Express
Find either the
  Winlink Express icon
    or the
  RMS Express icon
on your computer Desktop screen and double click it

## Slide 46: Configure Winlink Express
Under the Setting tab, select Winlink Express Setup

## Slide 47: Configure Winlink Express
  Fill out the Winlink Express Properties page with you callsign, address and grid square location etc….
  Create a password and remember it. 
  When finished click update

## Slide 48: Configure Winlink Express
  Click on the dropdown list to the right of “Open Session:” and select “Packet Winlink”

## Slide 49: Configure Winlink Express
  Click on “Open Session:”

## Slide 50: Configure Winlink Express
Click on Settings

## Slide 51: Packet Settings
Packet TNC Type: KISS
Packet TNC Model: NORMAL
Serial Port: TCP
TCP Host/Port: 127.0.0.1 8100
Packet Sound Modem (browse to SoundModem’s
folder location)
Automatically launch packet sound modem CHECK
TNC Parameters check 1200 Baud
Enable Ipoll CHECK
Automatically call when there are pending outping messages CHECK
Click on “Update” to close

## Slide 52: Restart Winlink Express
Close the Packet Winlink Session Window
Exit Winlink Express
Re-start Windows Express
At the top of Winlink program window, re-select a “Packet Winlink” session to the right of “Open Session:”
Click on “Open Session”

## Slide 53: Look for 3 Windows:
Winlink
soundmodem
The Winlink window,
The Packet Winlink Session window,
& the SoundModem window
Packet
Session

## Slide 54: Configure SoundModem
Select SignaLink as soundmodem audio devices

## Slide 55: Configure SoundModem

## Slide 56: Select Audio Devices
Under Settings select “Devices”

## Slide 57: Select Audio Devices

## Slide 58: Other Device Settings
Uncheck TX rotation
Check Single channel output
Check Color waterfall
AGWPE Server Port Uncheck Enabled
KISS Server Port 8100 & check Enabled
Select PTT Port NONE
Uncheck Dual PTT
Uncheck Swap COM pin
Click OK

## Slide 59: Modem Timing Settings
Under settings click “Modems”

## Slide 60: Soundmodem Modem Settings
Check KISS Optimization
Check non-AX25 filter
Under Modem type ch: A
Mode AFSK AX.25 1200bd
TXDelay 500 msec
Click on “OK”

## Slide 61: SoundModem Main Window Settings
Select AFSK AX.25 1200bd
Check Hold pointers

## Slide 62: Sending an Email Message

## Slide 63: Compose an E-mail message
Under Message Menu select New Message….

## Slide 64: Composing E-mail message
Select “Winlink Message”
Enter either Call Sign or an e-mail address
Area for typing message

## Slide 65: Post Message
After message is composed, click on
“Post to Outbox”

## Slide 66: Select Gateway
Click on Channel Selection

## Slide 67: Select Gateway
Select closest Gateway

## Slide 68: Set your Radio Frequency
Set your Radio Frequency to the Gateway’s Frequency

## Slide 69: Send E-mail
Click “Start”

## Slide 70: Winlink Client Sends Message
If not sent, then….. we’ll start debugging 

## Slide 72: BACKUP SLIDES
backup

## Slide 73: VARA FM (optional)
    Go to webpage  https://downloads.winlink.org/VARA%20Products/
    Download the file VARA%20FM%20v4.3.8%20setup.zip
    Extract and run the installation VARA%20FM%20setup%20 (Run%20as%20Administrator).exe similar to method used to install RMS winlink